## Slide 1: I-V Characteristics and Thevenin’s Theorem
Shadman Shahriar (SDS)
Lecturer, Brac University

## Slide 2: Finding the I-V Characteristics of a Linear Circuit
Find two data points that describe the circuit.
  Choose any voltage/current source of your choice
  Connect it to the two terminals of the linear circuit
  Find the voltage and current between the two terminals
  That’s your data point
  Repeat the same procedure for a different voltage/current
  Get a new data point
Find I-V characteristic equation from the two data points

## Slide 3: Finding the Thevenin’s Equivalent Circuit
Find the Thevenin’s Voltage
  Is one of your data point is like: ?
    If answer is yes, then:
      The in is your
    If answer is no, then:
      Find from the I-V characteristic equation
      Set and , to find
Find the Thevenin’s Resistance
  It’s just the inverse of :
Draw the Thevenin’s equivalent circuit

## Slide 4: Example 1

## Slide 5: Example 1 (Step 0)
Identify one of the terminals as the positive and the other as the negative terminal.

## Slide 6: Example 1 (Step 0)
Identify the direction of current following passive sign convention.

## Slide 7: Example 1 (Step 0)
In an I-V characteristics problem, we are always finding the relation between this and .

## Slide 8: Example 1 (Step 1)
Connect an voltage/current source (of any value you like) between the two terminals.

## Slide 9: Example 1 (Step 1)
I am choosing 0A current source because it is advantageous when finding Thevenin’s circuit.

## Slide 10: Example 1 (Step 1)
We can easily check that . Now, we have to find the value of .

## Slide 11: Example 1 (Step 1)
Let’s use Nodal analysis to find the value of .

## Slide 12: Example 1 (Step 1)
Let’s use Nodal analysis to find the value of .

## Slide 13: Example 1 (Step 1)
Let’s use Nodal analysis to find the value of .
yields
So, the data point is .

## Slide 14: Example 1 (Step 2)
Repeat the procedure (first step) to find a second data point.

## Slide 15: Example 1 (Step 2)
Let’s use . Now, we have to find the new value of .

## Slide 16: Example 1 (Step 2)
Let’s use Nodal analysis to find the new value of .

## Slide 17: Example 1 (Step 2)
Let’s use Nodal analysis to find the new value of .
yields
So, the data point is .

## Slide 18: Example 1 (Step 2)
Now that we have 2 data points, we can move on to either Thevenin or I-V characteristics.
Data points:

## Slide 19: Example 1 (Thevenin/Step 3)
Thevenin’s voltage is just the coordinate of the data point .

## Slide 20: Example 1 (Thevenin/Step 3)
Thevenin’s resistance is just the inverse of the slope .

## Slide 21: Example 1 (Thevenin/Step 3)
Now draw the Thevenin’s equivalent circuit from the values of and .

## Slide 22: Example 1 (Thevenin/Step 3)
Now draw the Thevenin’s equivalent circuit from the values of and .

## Slide 23: Example 1 (Thevenin)
can be negative, if is negative. (although, usually, it is positive.) It means, the “resistor” actually does not consume power, rather it supplies power. Of course there is no such resistor in real life, but one can be made from dependent sources.
Always keep track of which terminal is the positive terminal and which one is the negative terminal.
Negative terminal of should be near the negative terminal of the linear circuit and positive terminal of should be close to the positive terminal of the linear circuit.
Things to note in this Thevenin example…

## Slide 24: Example 1
Now from the 2 data points, we can also find the I-V characteristics of the circuit.
Data points:

## Slide 25: Example 1 (I-V/Step 3)
To draw the I-V characteristic graph, we can just plot the points and join them via a line.
Chart: 
| 4 | 0 | -20 | -18 | -22 | -40
Y-values | -12 | -10 | 0 | -1 | 1 | 10

## Slide 26: Example 1 (I-V/Step 3)
We can find the slope just like we did for Thevenin.

## Slide 27: Example 1 (I-V/Step 3)
We can find the slope just like we did for Thevenin.

## Slide 28: Example 1 (I-V/Step 3)
We can find the slope just like we did for Thevenin.

## Slide 29: Example 1 (I-V/Step 3)
We can find the slope just like we did for Thevenin.

## Slide 30: Example 1 (I-V/Step 3)
Here, we have used the straight line equation, Instead, we could have used the straight line equation with slope and through the point
Since is always one of the data points on the line,
Things to note in this I-V characteristics example…

## Slide 31: Example 2
\documentclass[margin=0pt]{standalone} % svg
% \documentclass[convert, margin=0pt]{standalone} % png, don't forget to change latex compiler
\usepackage{anyfontsize, amssymb, amsmath}
% \usepackage[shortlabels]{enumitem}
\usepackage[siunitx, american, RPvoltages]{circuitikz}
\sisetup{parse-numbers=false}
\usepackage{pgfplots}
\pgfplotsset{compat=1.18}
\usepackage[many]{tcolorbox}
% short-hand for resistor units, e.g.
% in circuitikz: 1<\MO>, 2<\mA>, 3<\kV>, 4<\uF>, 5<\nH>, 6<\C>
% in math-mode: \qty{1}{\MO}
\DeclareSIUnit{\mO}{\milli\ohm}
\DeclareSIUnit{\kO}{\kilo\ohm}
\DeclareSIUnit{\MO}{\mega\ohm}
\usepackage{xcolor}
\color{white}
\begin{document}
\begin{circuitikz}[x=1.5in, y=1.5in]
\draw (0,0)
-- ++(left:1)
to[V, l=120<\V>] ++(up:1)
to[I, l=3<\A>, invert, *-*] ++(right:1)
to[R, l=20<\ohm>, f>^=$i_x$, -*] ++(down:1)
-- ++(right:2)
node[right]{$b$}
to[open, o-o] ++(up:1)
node[right]{$a$}
-- ++(left:1)
to[R, l_=30<\ohm>, *-] ++(left:1)
++(left:1)
-- ++(up:0.5)
to[cV, l=$10i_x$] ++(right:1)
to[R, l=60<\ohm>]++(right:1)
-- ++(down:0.5)
;
\end{circuitikz}
\end{document}

## Slide 32: Example 2 (Step 0)
\documentclass[margin=0pt]{standalone} % svg
% \documentclass[convert, margin=0pt]{standalone} % png, don't forget to change latex compiler
\usepackage{anyfontsize, amssymb, amsmath}
% \usepackage[shortlabels]{enumitem}
\usepackage[siunitx, american, RPvoltages]{circuitikz}
\sisetup{parse-numbers=false}
\usepackage{pgfplots}
\pgfplotsset{compat=1.18}
\usepackage[many]{tcolorbox}
% short-hand for resistor units, e.g.
% in circuitikz: 1<\MO>, 2<\mA>, 3<\kV>, 4<\uF>, 5<\nH>, 6<\C>
% in math-mode: \qty{1}{\MO}
\DeclareSIUnit{\mO}{\milli\ohm}
\DeclareSIUnit{\kO}{\kilo\ohm}
\DeclareSIUnit{\MO}{\mega\ohm}
\usepackage{xcolor}
\color{white}
\begin{document}
\begin{circuitikz}[x=1.5in, y=1.5in]
\draw (0,0)
-- ++(left:1)
to[V, l=120<\V>] ++(up:1)
to[I, l=3<\A>, invert, *-*] ++(right:1)
to[R, l=20<\ohm>, f>^=$i_x$, -*] ++(down:1)
-- ++(right:2)
node[above]{$b$}
to[open, o-o] ++(up:1)
node[above]{$a$}
-- ++(left:1)
to[R, l_=30<\ohm>, *-] ++(left:1)
++(left:1)
-- ++(up:0.5)
to[cV, l=$10i_x$] ++(right:1)
to[R, l=60<\ohm>]++(right:1)
-- ++(down:0.5)
;
\color{green}
\draw (0,0)
++(right:1.8)
to[open, v>=$V$] ++(up:1)
to[open, i=$I$] ++(left:0.2)
;
\end{circuitikz}
\end{document}

## Slide 33: Example 2 (Step 1)
\documentclass[margin=0pt]{standalone} % svg
% \documentclass[convert, margin=0pt]{standalone} % png, don't forget to change latex compiler
\usepackage{anyfontsize, amssymb, amsmath}
% \usepackage[shortlabels]{enumitem}
\usepackage[siunitx, american, RPvoltages]{circuitikz}
\sisetup{parse-numbers=false}
\usepackage{pgfplots}
\pgfplotsset{compat=1.18}
\usepackage[many]{tcolorbox}
% short-hand for resistor units, e.g.
% in circuitikz: 1<\MO>, 2<\mA>, 3<\kV>, 4<\uF>, 5<\nH>, 6<\C>
% in math-mode: \qty{1}{\MO}
\DeclareSIUnit{\mO}{\milli\ohm}
\DeclareSIUnit{\kO}{\kilo\ohm}
\DeclareSIUnit{\MO}{\mega\ohm}
\usepackage{xcolor}
\color{white}
\begin{document}
\begin{circuitikz}[x=1.5in, y=1.5in]
\draw (0,0)
-- ++(left:1)
to[V, l=120<\V>] ++(up:1)
to[I, l=3<\A>, invert, *-*] ++(right:1)
to[R, l=20<\ohm>, f>^=$i_x$, -*] ++(down:1)
-- ++(right:2)
node[above]{$b$}
to[open, o-o] ++(up:1)
node[above]{$a$}
-- ++(left:1)
to[R, l_=30<\ohm>, *-] ++(left:1)
++(left:1)
-- ++(up:0.5)
to[cV, l=$10i_x$] ++(right:1)
to[R, l=60<\ohm>]++(right:1)
-- ++(down:0.5)
;
\color{green}
\draw (0,0)
++(right:1.8)
to[open, v>=$V$] ++(up:1)
to[open, i=$I$] ++(left:0.2)
;
\color{red}
\draw (0,0)
++(right:2)
node[circ]{}
-- ++(right:0.5)
to[I, l=0<\A>] ++(up:1)
-- ++(left:0.5)
node[circ]{}
;
\end{circuitikz}
\end{document}

## Slide 34: Example 2 (Step 1)
\documentclass[margin=0pt]{standalone} % svg
% \documentclass[convert, margin=0pt]{standalone} % png, don't forget to change latex compiler
\usepackage{anyfontsize, amssymb, amsmath}
% \usepackage[shortlabels]{enumitem}
\usepackage[siunitx, american, RPvoltages]{circuitikz}
\sisetup{parse-numbers=false}
\usepackage{pgfplots}
\pgfplotsset{compat=1.18}
\usepackage[many]{tcolorbox}
% short-hand for resistor units, e.g.
% in circuitikz: 1<\MO>, 2<\mA>, 3<\kV>, 4<\uF>, 5<\nH>, 6<\C>
% in math-mode: \qty{1}{\MO}
\DeclareSIUnit{\mO}{\milli\ohm}
\DeclareSIUnit{\kO}{\kilo\ohm}
\DeclareSIUnit{\MO}{\mega\ohm}
\usepackage{xcolor}
\color{orange}
\begin{document}
\begin{circuitikz}[x=1in, y=1in]
\draw (0,0)
node[circ]{}
node[ground]{}
++(-2,1)
node[left]{$V_1$}
++(right:1)
node[above]{$V_2$}
++(right:1)
node[above right]{$V_3$}
++(-1,0.5)
node[above]{$V_4$}
;
\end{circuitikz}
\end{document}

## Slide 35: Example 2 (Step 1)
\documentclass[margin=0pt]{standalone} % svg
% \documentclass[convert, margin=0pt]{standalone} % png, don't forget to change latex compiler
\usepackage{anyfontsize, amssymb, amsmath}
% \usepackage[shortlabels]{enumitem}
\usepackage[siunitx, american, RPvoltages]{circuitikz}
\sisetup{parse-numbers=false}
\usepackage{pgfplots}
\pgfplotsset{compat=1.18}
\usepackage[many]{tcolorbox}
% short-hand for resistor units, e.g.
% in circuitikz: 1<\MO>, 2<\mA>, 3<\kV>, 4<\uF>, 5<\nH>, 6<\C>
% in math-mode: \qty{1}{\MO}
\DeclareSIUnit{\mO}{\milli\ohm}
\DeclareSIUnit{\kO}{\kilo\ohm}
\DeclareSIUnit{\MO}{\mega\ohm}
\usepackage{xcolor}
\color{white}
\def\vv#1{\textcolor{orange}{V_{#1}}}
\begin{document}$
\begin{aligned}
& \because \qty0\A\text{ dummy source }\implies\therefore I = 0 \\
\\
& \vv 1 - 0 = 120 \\
& \vv 4 - \vv 1 = 10i_x \\
& i_x = \frac{\vv 2 - 0}{20} \\
& \text{\underline{\textbf{KCL@2:}}} \\
& \quad \vv 2\left(\frac{1}{20} + \frac{1}{30}\right) - \frac{0}{20} - \frac{\vv 3}{30} + 3 = 0 \\
& \text{\underline{\textbf{KCL@3:}}} \\
& \quad \vv 3\left(\frac{1}{60} + \frac{1}{30}\right) - \frac{\vv 4}{60} - \frac{\vv 2}{30} - 0 = 0 \\
& \text{\underline{\textbf{Solving:}}} \\
& \quad \vv 1 = 120,~\vv 2 = -30,~\vv 3 = 15,~\vv 4 = 105,~i_x = -1.5 \\
\\
& \therefore \vv {Th} = \vv a - \vv b = \vv 3 - 0 = 15 \\
& \therefore\text{ Our first data point is }(15,0).
\end{aligned}
$\end{document}

## Slide 36: Example 2 (Step 2)
\documentclass[margin=0pt]{standalone} % svg
% \documentclass[convert, margin=0pt]{standalone} % png, don't forget to change latex compiler
\usepackage{anyfontsize, amssymb, amsmath}
% \usepackage[shortlabels]{enumitem}
\usepackage[siunitx, american, RPvoltages]{circuitikz}
\sisetup{parse-numbers=false}
\usepackage{pgfplots}
\pgfplotsset{compat=1.18}
\usepackage[many]{tcolorbox}
% short-hand for resistor units, e.g.
% in circuitikz: 1<\MO>, 2<\mA>, 3<\kV>, 4<\uF>, 5<\nH>, 6<\C>
% in math-mode: \qty{1}{\MO}
\DeclareSIUnit{\mO}{\milli\ohm}
\DeclareSIUnit{\kO}{\kilo\ohm}
\DeclareSIUnit{\MO}{\mega\ohm}
\usepackage{xcolor}
\color{white}
\def\vv#1{\textcolor{orange}{V_{#1}}}
\begin{document}$
\begin{aligned}
& \because \qty1\A\text{ dummy source }\implies\therefore I = 1 \\
\\
& \vv 1 - 0 = 120 \\
& \vv 4 - \vv 1 = 10i_x \\
& i_x = \frac{\vv 2 - 0}{20} \\
& \text{\underline{\textbf{KCL@2:}}} \\
& \quad \vv 2\left(\frac{1}{20} + \frac{1}{30}\right) - \frac{0}{20} - \frac{\vv 3}{30} + 3 = 0 \\
& \text{\underline{\textbf{KCL@3:}}} \\
& \quad \vv 3\left(\frac{1}{60} + \frac{1}{30}\right) - \frac{\vv 4}{60} - \frac{\vv 2}{30} - 1 = 0 \\
& \text{\underline{\textbf{Solving:}}} \\
& \quad \vv 1 = 120,~\vv 2 = -18,~\vv 3 = 45,~\vv 4 = 111,~i_x = -0.9 \\
\\
& \therefore \vv {ab} = \vv a - \vv b = \vv 3 - 0 = 45 \\
& \therefore\text{ Our second data point is }(45,1).
\end{aligned}
$\end{document}

## Slide 37: Example 2 (Step 3: Thevenin & I-V)
\documentclass[margin=0pt]{standalone} % svg
% \documentclass[convert, margin=0pt]{standalone} % png, don't forget to change latex compiler
\usepackage{anyfontsize, amssymb, amsmath}
% \usepackage[shortlabels]{enumitem}
\usepackage[siunitx, american, RPvoltages]{circuitikz}
\sisetup{parse-numbers=false}
\usepackage{pgfplots}
\pgfplotsset{compat=1.18}
\usepackage[many]{tcolorbox}
% short-hand for resistor units, e.g.
% in circuitikz: 1<\MO>, 2<\mA>, 3<\kV>, 4<\uF>, 5<\nH>, 6<\C>
% in math-mode: \qty{1}{\MO}
\DeclareSIUnit{\mO}{\milli\ohm}
\DeclareSIUnit{\kO}{\kilo\ohm}
\DeclareSIUnit{\MO}{\mega\ohm}
\usepackage{xcolor}
\color{white}
\def\vv#1{\textcolor{orange}{V_{#1}}}
\begin{document}
\pagecolor{black}
$
\begin{aligned}
m & = \frac{\Delta y}{\Delta x} = \frac{y_2-y_1}{x_2-x_1} \\
& = \frac{\qty{(1-0)}{\A}}{\qty{(45-15)}{\V}} = \frac{\qty{1}{\A}}{\qty{30}{\V}} \\
& = \qty{\frac{1}{30}}{\per\ohm} \\
\end{aligned}
$\end{document}
From the two data points and , we have,

## Slide 38: Example 2 (Thevenin/Step 3)
\documentclass[margin=0pt]{standalone} % svg
% \documentclass[convert, margin=0pt]{standalone} % png, don't forget to change latex compiler
\usepackage{anyfontsize, amssymb, amsmath}
% \usepackage[shortlabels]{enumitem}
\usepackage[siunitx, american, RPvoltages]{circuitikz}
\sisetup{parse-numbers=false}
\usepackage{pgfplots}
\pgfplotsset{compat=1.18}
\usepackage[many]{tcolorbox}
% short-hand for resistor units, e.g.
% in circuitikz: 1<\MO>, 2<\mA>, 3<\kV>, 4<\uF>, 5<\nH>, 6<\C>
% in math-mode: \qty{1}{\MO}
\DeclareSIUnit{\mO}{\milli\ohm}
\DeclareSIUnit{\kO}{\kilo\ohm}
\DeclareSIUnit{\MO}{\mega\ohm}
\usepackage{xcolor}
\color{white}
\def\vv#1{\textcolor{orange}{V_{#1}}}
\begin{document}
\pagecolor{black}$
\begin{aligned}
\therefore R_{Th} & = \frac1m = \frac{1}{\qty{\frac{1}{30}}{\per\ohm}} = \qty{30}{\ohm}
\end{aligned}
$\end{document}

## Slide 39: Example 2 (Thevenin/Step 3)
\documentclass[margin=0pt]{standalone} % svg
% \documentclass[convert, margin=0pt]{standalone} % png, don't forget to change latex compiler
\usepackage{anyfontsize, amssymb, amsmath}
% \usepackage[shortlabels]{enumitem}
\usepackage[siunitx, american, RPvoltages]{circuitikz}
\sisetup{parse-numbers=false}
\usepackage{pgfplots}
\pgfplotsset{compat=1.18}
\usepackage[many]{tcolorbox}
% short-hand for resistor units, e.g.
% in circuitikz: 1<\MO>, 2<\mA>, 3<\kV>, 4<\uF>, 5<\nH>, 6<\C>
% in math-mode: \qty{1}{\MO}
\DeclareSIUnit{\mO}{\milli\ohm}
\DeclareSIUnit{\kO}{\kilo\ohm}
\DeclareSIUnit{\MO}{\mega\ohm}
\usepackage{xcolor}
\color{white}
\def\vv#1{\textcolor{orange}{V_{#1}}}
\begin{document}
\pagecolor{black}$
\begin{aligned}
\therefore V_{Th} & = \qty{15}{\V}
\end{aligned}
$\end{document}
From the data point , we get,

## Slide 40: Example 2 (I-V/Step 3)
\documentclass[margin=0pt]{standalone} % svg
% \documentclass[convert, margin=0pt]{standalone} % png, don't forget to change latex compiler
\usepackage{anyfontsize, amssymb, amsmath}
% \usepackage[shortlabels]{enumitem}
\usepackage[siunitx, american, RPvoltages]{circuitikz}
\sisetup{parse-numbers=false}
\usepackage{pgfplots}
\pgfplotsset{compat=1.18}
\usepackage[many]{tcolorbox}
% short-hand for resistor units, e.g.
% in circuitikz: 1<\MO>, 2<\mA>, 3<\kV>, 4<\uF>, 5<\nH>, 6<\C>
% in math-mode: \qty{1}{\MO}
\DeclareSIUnit{\mO}{\milli\ohm}
\DeclareSIUnit{\kO}{\kilo\ohm}
\DeclareSIUnit{\MO}{\mega\ohm}
\usepackage{xcolor}
\color{white}
\def\vv#1{\textcolor{orange}{V_{#1}}}
\begin{document}
\pagecolor{black}$
\begin{aligned}
y-y_1 & = m (x-x_1) \\
\implies y-0 & = \frac{1}{30} (x-15) \\
\implies y & = \frac{1}{30}x-\frac{15}{30} \\
\therefore y & = \frac{1}{30}x - \frac{1}{2} \\
\therefore I & = \frac{1}{30}V - \frac{1}{2}
\end{aligned}
$\end{document}
From slope and the data point , we get the equation of line,

## Slide 41: Example 2 (Step 1)
\documentclass[margin=0pt]{standalone} % svg
% \documentclass[convert, margin=0pt]{standalone} % png, don't forget to change latex compiler
\usepackage{anyfontsize, amssymb, amsmath}
% \usepackage[shortlabels]{enumitem}
\usepackage[siunitx, american, RPvoltages]{circuitikz}
\sisetup{parse-numbers=false}
\usepackage{pgfplots}
\pgfplotsset{compat=1.18}
\usepackage[many]{tcolorbox}
% short-hand for resistor units, e.g.
% in circuitikz: 1<\MO>, 2<\mA>, 3<\kV>, 4<\uF>, 5<\nH>, 6<\C>
% in math-mode: \qty{1}{\MO}
\DeclareSIUnit{\mO}{\milli\ohm}
\DeclareSIUnit{\kO}{\kilo\ohm}
\DeclareSIUnit{\MO}{\mega\ohm}
\usepackage{xcolor}
\color{orange}
\begin{document}
\begin{circuitikz}[x=1in, y=1in]
\draw (0,0)
node[circ]{}
node[ground]{}
++(-2,1)
node[left]{$V_1$}
++(right:1)
node[above]{$V_2$}
++(right:1)
node[above right]{$V_3$}
++(-1,0.5)
node[above]{$V_4$}
;
\end{circuitikz}
\end{document}

## Slide 42: Example 1 (Step 2)
Repeat the procedure (first step) to find a second data point.